## Slide 1: Project LED Playground
Date: 21/06/2026
ISPACE
v 0.1
A LED matrix display designed using Configuration Logic Blocks to create animations and emojis

## Slide 2: Version History
Version | Date | Description | Remarks
0.1 | 21-06-2026 | Initial draft | 

## Slide 3: Introduction
There are many ready-made LED matrices available online that are simple to use and low-cost. However, the intention behind designing one from scratch is to understand the adaptation of CLB technology in generic applications for achieving lower cost and better battery performance.
The design will be based on Microchip’s latest CLB MCU (PIC18F26). Since CLB was introduced only recently, it is still relatively unknown to the wider engineering community, mainly because its adoption has been limited to niche application.
The CLB is a reconfigurable digital logic module, similar to a CPLD, that is integrated into the microcontroller (MCU) and performs hardware-based digital logic independent of the CPU. This results in fast and predictable response times for a diverse range of applications, such as automotive and industrial.
The CLB enables much larger hardware-based digital logic designs than previously possible on an MCU (up to 128 Basic Logic Elements, or BLEs) and is also capable of operating in sleep mode, allowing complex processing to occur with very low power consumption.
…
Image courtesy: Adafruit, Waveshare

## Slide 4
V0.1

## Slide 5: V0.1 Implementation
*design may vary during implementation
Row LEDs
Column LEDs
Front side / LED PCB
Back side / CTRL PCB
CLB
3V CELL
RTC
LP
MCU
TH
SNS
LP
PMIC
LED,
BTN
CLB: Configurable Logic Block
LP MCU: Low Power MCU
RTC: Real Time Clock
TH SNS: Temperature Sensor
LP PMIC: Low Power PMIC
XTAL: External Crystal
USBC: USB-C Connector
XTAL
USBC

## Slide 6: High Level Block Diagram V0.1
*Part may be changed per availability
RTC
(RV-8263-C7)
Temperature
Sensor
(HDC3022)
BLE
ANT
XTAL
3V
I2C
GPIOs
SPI
Debug
Connector
+
UCB-C
EXT/BATT_IN
SDI/UART
LEDs + BTN
LP PMIC
(nPM2100)
3V Coin Cell
LP MCU
(nRF52840)
LED CTRL
Configurable Logic Block
(PIC18F26Q35)
USB
Discrete LED matrix

## Slide 7: V0.1 working
*Implementation may vary during final release